## Slide 1: New generation of display for a smarter world

## Slide 2: What is missing? What are the remaining challenges?
Brightness
Low power
Resolution
Field of View
size and weight
Real time object classification
Immersive FoV
Social rejection
User-friendly interfaces
Digital fatigue
Use case
Road ahead is still long …

## Slide 3: Keep on being pioneer in DISplay
success stories for 40 years
Next big thing on Micro LED

## Slide 4: Leti’s fields
HMD
glasses (VR/AR/MR)
HuD
From display to
Augmented Reality (AR)
Large display
and true light field
Micro-display technology
&
Optical system
Leti’s value lies in our ability to have ongoing work on
components and optical system…

## Slide 5: micro-led array Platform
Epitaxy on patterned substrates & native color
LED array process pixelization down to 3 µm
3D integration technique of LED arrays on CMOS
Curved display to simplify the optics
IC silicon active matrix for LED driving
QDs and nanophosphors
2D layers
Micro-LED
Key achievements in 2017
Microdisplay monochrome 3 µm pitch
Microdisplay WXGA monochrome 10µm pitch
Advances in Display Technologies VIII
High-resolution active-matrix 10-um pixel-pitch GaN LED microdisplays for augmented reality applications [10556-17]
1 February 2018 11:00 AM

## Slide 6: What is inside ?
Epitaxy on patterned substrates & native color
LED array process pixelization down to less than 3 µm
3D integration technique of LED arrays on CMOS
IC silicon active matrix for LED driving
QDs and nanophosphors
2D layers
Curved display to simplify the optics
Key
facts
Led structure growth on various substrates
Self aligned patterning technology
Different hybridization technologies for different needs
ASIC design dedicated to microLED requirements
Color conversion implementation
Integrate optical system constraint on the display

## Slide 7: What is inside ?
Epitaxy on patterned substrates & native color
Led array process pixelization down to less than 3 µm
3D integration technique of LED arrays on CMOS
IC silicon active matrix for LED driving
QDs and nanophosphors
2D layers
Curved display to simplify the optics
Key
facts
Led structure growth on various substrates
Self aligned patterning technology
Different hybridization technologies for different needs
ASIC design dedicated to microLED requirements
Color conversion implementation
Integrate optical system constraint on the display

## Slide 8: What is inside ?
Epitaxy on patterned substrates & native color
LED array process pixelization down to less than 3 µm
3D integration bonding of Led arrays on CMOS
IC silicon active matrix for LED driving
QDs and nanophosphors
2D layers
Curve display to simplify the optics
Cu
SiO2
Key
facts
Led structure growth on various substrates
Self aligned patterning technology
Different hybridization technologies for different needs
ASIC design dedicated to microLED requirements
Color conversion implementation
Integrate optical system constraint on the display

## Slide 9: What is inside ?
Epitaxy on patterned substrates & native color
LED array process pixelization down to less than 3 µm
3D integration bonding of LED arrays on CMOS
IC silicon active matrix for Led driving
QDs and nanophosphors
2D layers
Curve display to simplify the optics
Key
facts
Led structure growth on various substrates
Self aligned patterning technology
Different hybridization technologies for different needs
ASIC design dedicated to microLED requirements
Color conversion implementation
Integrate optical system constraint on the display

## Slide 10: What is inside ?
Epitaxy on patterned substrates & native color
LED array process pixelization down to less than 3 µm
3D integration bonding of LED arrays on CMOS
IC silicon active matrix for LED driving
QDs and nanophosphores
2D layers
Curve display (xx°) to simplify the optics
Key
facts
Led structure growth on various substrates
Self aligned patterning technology
Different hybridization technologies for different needs
ASIC design dedicated to microLED requirements
Color conversion implementation
Integrate optical system constraint on the display

## Slide 11: What is inside ?
Epitaxy on patterned substrates & native color
LED array process pixelization down to less than 3 µm
3D integration technique of LED arrays on CMOS
IC silicon active matrix for LED driving
QDs and nanophosphors
2D layers
Curve display (xx°) to simplify the optics
Key
facts
Led structure growth on various substrates
Self aligned patterning technology
Different hybridization technologies for different needs
ASIC design dedicated to microLED requirements
Color conversion implementation
Integrate optical system constraint on the display
Photonic Instrumentation Engineering V
Curved sensors for compact high-resolution wide field designs: prototype demonstration and optical characterization
1 February 2018 02:40 PM

## Slide 12
native color solution
IQE of 31% @ 536 nm, 17% @566nm, 10% @ 598 nm and 2,7% @ 617 nm
What are the obstacles?
Donor
InGaNOS substrate
GaN template
Strained InGaN layer (~200 nm)
Sapphire substrate
Burried Oxyde
(~600 nm)
Transferred relaxed InGaN layer (~100 nm)
Soitec Smart cutTM technology
First
Results
Next steps light extraction and towards smaller mesa as small as 10µm pitch for micro-LED
Light-Emitting Diodes: Materials, Devices, and Applications for Solid State Lighting XXII
30 January 2018 11h40 am

## Slide 13: From Microdisplay to large display: What’s new ?
Could Micro-LED challenge LCD or OLED?
Majors are driving and maturing the market : Sony, Samsung, Apple, ….
Still many challenges to get an industrial solution …
Leti’s novel
proposal*
*Patented solution
Micro-Led wafer with driving electronic
 microLED with its CMOS
 Transfer & assembly
A modular solution with no need of TFT backplane

## Slide 14: and on optical systems …
HMD
HuD
Light field
Towards non-conventional, lens-free, see-through glasses
A bio-inspired / multi-channel approach
Single lens system
Leti’s solution
High resolution displays
Micro Lens Arrays
Optical design
Computational imaging
Calibration
Light field : multi views approach
A large scope of technologies to meet market challenges …

## Slide 15: Takeaway
Nomadic information bringing innovation and new market opportunity for display.
The available products and concepts are still at their infancy and a number of challenges are yet to be addressed
brightness, resolution, full color combined with large field of view, power consumption, system compactness and user interaction.
Leti’s mission: To develop new better products with industrial partners on challenging topics
Large field of view displays and systems for augmented reality
Efficient native color microdisplay
Simplified, low cost Large display
If you share our vision and want to take on challenges with us …
Please contact-us!
Team up with Leti and get value with optical devices

## Slide 16
Sylvie Joly
Display Business Developer, Optics and Photonics Division
 Sylvie-j.joly@cea.fr
 +33 6 45 15 02 98
Meet Leti experts at Booth #431 French Pavilion
South Hall